## Slide 1
RADIO COMMUNICATIONS
AN INTRODUCTION TO THE ELECTROMAGNETIC SPECTRUM
LESSON 2

## Slide 2
TIMELINE
RADIO COMMUNICATIONS
1864: James Clerk Maxwell describes radio wave mathematically
1888: Heinrich Hertz generates radio waves
1890: Detection of radio waves
1896: Guglielmo Marconi makes the first radio transmission
1915: Vacuum tubes are invented
1948: Transistor unveiled and patented
1960: First US communication satellite launched
1981: Cellular technology deployed
Radio, or radio communication, means any transmission and reception of signals, sounds, or intelligence of any nature by means of electromagnetic waves propagated in space. Examples of radio communication systems:
Radio broadcasting
TV broadcasting
Satellite communications
Mobile cellular telephony
Wireless local area network (LAN)
THE HISTORY OF RADIO

## Slide 3
THE RADIO SPECTRUM
Frequency | Range | Applications
Low frequency | 30-300 kHz | Navigation, time standards
Medium frequency | 300 kHz-3MHz | Marine/aircraft navigation, AM broadcast
High frequency (shortwave) amateur radio | 3-30 MHz | Broadcasting, mobile radio
Very high frequency | 30-300 MHz | Land mobile, FM/TV broadcast, amateur radio
Ultra high frequency | 300 MHz-3 GHz | Cell/mobile phones, WLAN, personal area networks (PANs)
Super high frequency | 3-30 GHz | Satellite, radar, backhaul, TV
Extremely high frequency | 30-300 GHz | Satellite, radar, backhaul, experimental

## Slide 4
MODULATION & TRANSMITTING DATA
The process of varying one or more properties of a periodic waveform, called the carrier signal, with a modulating signal that typically contains information to be transmitted. Modulation, which is how data is superimposed on the carrier, is a reversible operation. Demodulation is how the data is “read” by the receiving person or system. To be transmitted, information (data) must be transformed into electromagnetic signals.
Analog modulation: Varying the amplitude of the carrier wave.
Frequency modulation: Varying the frequency of the carrier wave.
Phase modulation: Varying the phase of the carrier wave through a variety of techniques, including Frequency Shift Keying (FSK), Binary Phase Shift Keying (BPSK), Gaussian Minimum Shift Keying (GMSK), and Quadrature Phase Shift Keying (QPSK), among others.
WHAT IS BANDWIDTH?
Bandwidth represents a frequency range measured in Hertz. If a signal’s frequency or spectrum extends over a wide range, the signal has a large bandwidth. Bandwidth directly correlates to the communications capacity of the signal.
BASIC STRUCTURE
Transmitter: Modulation, coding
Transmission channel: Loss or attenuation, distortion, interference, noise
Receiver: Amplification, demodulation and decoding, filtering
RADIO WAVES

## Slide 5
This concept spreads data over a wide bandwidth. The bandwidth of the signal W is much greater than the original message bandwidth (or the signaling rate R).
Transmission bandwidth is independent of the message. The applied code is known both to the transmitter and receiver.
Spectrum spread makes jamming and interception harder.
Frequency hopping is a method in which you broadcast over a seemingly random series of frequencies.
Direct sequence is a technique in which each bit is represented by multiple bits along a transmitted signal using a “chipping” code.
SPECTRUM SPREAD

## Slide 6
MULTIPLEXING TECHNIQUES
FREQUENCY DIVISION MULTIPLEXING (FDM)
The basis for broadcast radio; several stations can transmit simultaneously without interfering with each other provided they use separate carrier frequencies. A channel gets the whole spectrum for a certain amount of time (orthogonal).
Advantages:
No dynamic coordination needed
Works for analog and digital signals
Low bit rates – cheaper, delays are spread
CODE DIVISION MULTPLEXING (CDM)
TIME DIVISION MULTIPLEXING (TDM)
A channel gets the whole spectrum for a certain amount of time (orthogonal).
Advantages:
Only one carrier in the medium at a time
The throughput is high, which support bursts
More flexible; multiple slots
Disadvantages:
Framing and precise synchronization necessary
High bit rates at each transmitter and receiver
Each channel had a unique code (not necessarily orthogonal). All channels use the same spectrum at the same time.
Advantages:
Bandwidth efficiency
No coordination or synchronization needed
Good protection against interference and tapping
Disadvantages:
Lower user data rates due to high gains required to reduce interference
More complex signal regeneration

## Slide 7
IMPROVING RADIO COMMUNICATIONS
Options include:
Higher power transmitter
Better antenna gain
Higher antennas for increased line-of-sight
More sensitive receivers, which can detect a weaker signal
Move transmitter and receiver closer together to increase power
Use lower frequencies – a longer wavelength has less absorption
TRANSMISSION FACTORS
Propagation characteristics differ with the environment through and over which radio waves travel. Factors include terrain, vegetation, buildings, atmospherics, and water surfaces. Interference from other sources and noise will impact signal behavior as well, including co-channel and adjacent channel interference or ambient noise from the radio transmitter components or other electronic devices.
FREE-SPACE PATH LOSS
For free-space path loss, the signal is proportional to the inverse of the distance squared. For example, if the distance between transmitter and receiver doubles power, the power level at the receiver is reduced by 1/4. If the distance triples, the power at the receiver is reduced by 1/9.
PROPAGATION